## Slide 1
Stage A · µCT → Allen CCF
Working today — tested on real µCT. Rigid + optional landmark TPS is solid; the deformable refiners are wrappers with known limits.
INPUT µCT OME-Zarr (µm voxels, GB scale) → REFERENCE BrainGlobe Allen CCF → OUTPUT warped sample on the CCF voxel grid
init
prealign
refine
landmarks
alignFull
METHOD
Reference. Allen CCF via BrainGlobe (atlas_name).
Display. napari MIP, strided preview ≤ 192³ — RAM bounded regardless of source size.
Rigid pose. 6 sliders (3 translations µm, 3 rotations °) + axis-flip checkboxes; live resample onto CCF grid.
Crop ROI. 6 min/max sliders crop the CCF to a bbox around the sample.
Refine. ±3 mm / ±30° in axial / coronal / sagittal ortho views.
Landmarks. optional Procrustes / Kabsch refit on ≥3 paired clicks.
Production warp. alignFull warps the full OME-Zarr at every pyramid level, one output chunk at a time via dask_image.ndinterp.
STATE & MATH
Coords. everything in (z, y, x) µm. No unit-tagging schema.
Rigid. output_µm = R · F · (input_µm − c) + c + t, with R = intrinsic ZYX Euler, F = ±1 axis flips, c = sample center, t = translation.
Optional TPS. thin-plate spline on the residuals between rigid prediction and landmark clicks; vanishes far from landmarks → rigid preserved.
State file. one state.json per stage: {sample_zarr, voxel_um, sample_level, atlas_name, transform, landmarks, ccf_crop_bbox, history}. Resume any step.
Output. uct_in_ccf.zarr — multiscale OME-Zarr, chunked, CCF voxel grid. Used directly as Stage B's reference.
Stage A — µCT to CCF
1 / 2

## Slide 2
Stage B · EM → aligned µCT (proposed)
Roadmap — not yet implemented and not yet tested on EM data.
⚠ ROADMAP — --reference, alignFull --tps, voxel-aware UI all unmerged. No EM volume has been run through this pipeline.
PROPOSED INPUT EM OME-Zarr (nm voxels, TB scale) → PROPOSED REFERENCE uct_in_ccf.zarr → PROPOSED OUTPUT warped EM on the CCF voxel grid
init --reference
prealign
refine
landmarks
alignFull --tps
WHAT WOULD CHANGE vs STAGE A (to be built)
Reference loader. add load_zarr_reference(path) alongside load_ccf. ~6 one-line edits.
Voxel scale. 4 nm stored as 0.004 µm. No unit conversion.
UI scaling. slider step, preview stride, landmark marker size derive from sample_voxel_um.
Warp composition. alignFull --tps composes Rigid ∘ TPS per chunk. B-spline plugs in later.
DESIGN TARGET (reuses Stage A engine — proven on µCT)
RAM bound (proven on µCT). warp reads one output chunk's source-bbox at a time.
Parallelism (proven on µCT). chunks via ThreadPoolExecutor; bypasses dask graph build.
State (designed). state_em.json adds reference_zarr. state_uct.json unchanged.
Open risks. nm-scale slider/click ergonomics, OME-Zarr level-selection on TB inputs, TPS conditioning on nm landmark spreads — all untested.
Out of scope. EM section assembly (TrakEM2 / render-python).
Stage B — EM to aligned µCT
2 / 2